## Slide 1
Verify payment
Check GPS location
Set bike status
Control buzzer & LED
Buzzer & LED
GPS Module
E-ink Display
GPRS Module
Environmental Sensors
Battery
Custom Hardware Module
ESP
Reply to requests
Store IOTA transactions in Tangle
IOTA Node
Make anonymous payment (pre-paid) via IOTA
User
Request/
IOTA transaction with sensor data
Request response
Key advantages:
Open-source
No app, no backend
No personal data
Secured, immutable, anonymous payment
Generalistic (any moveable object you can rent)
Solar Module
V 1.0
Scan QR Code of receiving address

## Slide 2
Update receiving address for each session
Verify payment
Check GPS location
Set bike status
Control buzzer & LED
Buzzer & LED
GPS Module
E-ink Display
GPRS Module
Environmental Sensors
Battery
Custom Hardware Module
ESP
Reply to requests
Store IOTA transactions in Tangle
IOTA Node
Make anonymous payment (pre-paid) via IOTA
User
Request/
IOTA transaction
Request response
Solar Module
V 2.0
Scan QR Code of receiving address
Visualize positions of bike in network
Visualize environmental data
Visualize user bike track
Server
Added advantages:
Visualization of hardware network and sensor data
Collected data can be offered to marketplace
Sensor data
(environmental, GPS)
IOTA transaction/Sensor data

## Slide 3
State diagram of hardware module
Parked
Parked
Rented
Stolen
gps_loc_parked
curr_loc - gps_loc_parked
> trigger_dist
curr_loc - gps_loc_parked
< trigger_dist
or curr_loc remains relatively unchanged for 60s
trigger_pressed and balance > 0
elapsed_time > curr_balance * time_multiplier

## Slide 4
"Parked" loop
Check if trigger button is pressed
  If true: get_balance()
Send to server all data
Loop 10 times
  Go to sleep
  Wake up every 60 seconds
  Take sensor data
  check_if_stolen()
    If true: get start_loc,
    get start_time,
    break loop
get_balance()
Loop 10 times
Get account balance B
  If B = 0: delay 10s
  If B > 0: status = rented, break loop
check_if_stolen()
curr_loc – gps_loc_parked > trigger_dist
  If true: status = stolen,
  If false: status = parked
"Rented" loop
Collect sensor data & send to server
Check balance for top-ups
Check if session expires
  If true: status = parked,
  update receiving address,
  break loop
"Stolen" loop
check_if_stolen()
  If false: break loop
  If true:
    loc_avg = (start_loc + curr_loc)/2,
    If time > 60 seconds:
      If (loc_avg – start_loc) < trigger_dist:
        status = parked,
        gps_loc_parked = loc_avg,
        break loop

## Slide 5
Database
HARDWARE_STATUS
*hardwareID | integer
address_index | integer
session_address | text
status | text
latittude | real
longitude | real
SENSOR_DATA
*index | big serial
hardwareID | integer
address | text
latitude | real
longitude | real
temperature | real
humidity | real
timestamp | timestamp with timezone
*hardwareID – key (unique) attribute